## Slide 1: Gradiometers for Planetary Science
Mark Lindeman 2-20-2026

## Slide 2: Jupiter Is a Huge Rotating Magnet
Jupiter's Magnetic field is 100s of nanotesla (nT) at Europa’s orbit
May induce electrical currents in conducting materials
The Galileo Spacecraft observed a magnetic response from Europa
Margaret Kivelson Group at UCLA identified a magnetic dipole signal from Europa
Attributed to salty oceans under several km ice
Europa’s
Magnetic Response
Ocean Model
Jupiter Magnetic Field

## Slide 3: Look for magnetic signals on water worlds
Look for magnetic signals due to
  Water in lakes and veins in the ice
  Variations in ocean depth
  Geysers
  Ocean floor vents
  Magnetic signals to due water flowing (magnetohydrodynamics)
  Subsurface electrical currents
Small features require a more sensitive magnetometer

## Slide 4: Convection and Geology
Predicted underwater plumes of highly saline water
Predicted convection, layering, Diffusion dynamics in Europan ocean
  primarily composed of aqueous Na2SO4 and MgSO4, for both a saturated and a dilute concentrations
Expect greatly varying conductivity in plumes, layers, and currents
Should result in fine scale magnetics signals
What if we could map these magnetic signals?

## Slide 5: New Asteroid Science:
Ceres is a possible water world
  Geological features suggest brine under the ice
  Solar wind may induce a weak magnetic response from the subsurface brine
Previously undetectable asteroids
  Fluxgates were not able to detect magnetism of low magnetism asteroids
  These include on Eros, Lutetia, 67P, Braille, Steins, etc.
  Map the weak magnetic fields of these objects
  Provide evidence about composition and evolution
Solar wind induced signals from metallic parts
Eros

## Slide 6: Uranus system
The Uranus is system is called out in the Decadal system
Moons are likely water worlds:
  Ariel
  Umbriel
  Titania
  Oberon
Also the Magnetosphere of Uranus offers interesting plasma physics to study between visits to moons using a sensitive highfrequency range magnetometer (MHz)
  What if we had magnetometer with sensitivy far exceeding fluxgates over bandpass between 0 Hz – 10s of MHz instead of 0-20 Hz?
Uranus and Moons

## Slide 7: Idea: low gradient fields induce high gradient response
Jupiter applies a varying magnetic field to Europa
This induces electrical current in conductive regions (of ocean)
Spatial variation in conductivity results in local variations in the magnetic field gradient
These local features can have a steeper gradient then the nonlocal large-scale fields from distant sources
Provides a sensitive probe of local variations in conductivity or magnetism under the surface
Gradiometer measures the first derivative of the magnetic which is large near sources, but falls off as r-4
External field from Jupiter or Solar Wind
(blue)
Induced field gradient from conductive regions
(green)
The induced magnetic field has a larger gradient than the solar wind field
Conductive Region

## Slide 8: Measure Magnetic Gradients from Orbit
Conductivity Features of Ocean (grey)
Induced Magnetic Gradient Features
(rainbow)
Magnetic field Vectors
Orbit 100 km above surface
Measure Magnetic Gradients to Observe Magnetic Features

## Slide 9: Why Use Magnetic Gradiometer?
Picks out nearby sources like magnetic areas in planetary objects
Detects electrically conductive regions through their magnetic response to ambient fields
Even though the magnetic field is very smooth, the gradient is not smooth
  Information about the magnetic structure of the body
Filters out large scale noise sources like the solar wind
Conductivity of Ocean (grey)
Induced Magnetic Gradient at 100 km (rainbow)
Magnetic field Vectors

## Slide 10: Solar Wind Magnetic Noise
Issue: Solar Wind May Overwhelm Signals
  Solar Wind is a source of magnetic noise varying up to 100 nT level near earth
  nT magnetic fluctuations dominate signals we want to detect
  Want to detect pT or smaller signals from small scall planetary features
About the solar wind:
  Though the magnetic field varies a lot over time, it is fairly uniform on meter to kilometer scales
Solution: use a gradiometer configuration to effectively null out solar wind
  Local magnet sources have a significant gradient on this scale

## Slide 11: Filtering by Gradiometer
Gradiometer removes long wavelength, low frequency magnetic signals from solar wind
Removes long term correlations in the solar wind noise
Preserves signals from nearby magnetic sources
  These have much steeper gradients
Modeling predicts noise filtered to ~ 1 ft/m
  Easily sufficient to measure planetary magnetic gradients
Suppress
Raw Solar Wind Noise
Filtered Solar Wind Noise

## Slide 12: Modeling of Gradients

## Slide 13: Magnetic Field Model
Model magnetic field gradients to verify implementation is practical
Conductivity is modeled as a thin shell
Ambient oscillating magnetic field from Jupiter
Faraday’s law: magnetitic fields normal to the surface induce toroidal currents on the sphere
  Toroidal = no divergence, has curl
Current produces emitted fields
Self consistently solve for currents and emitted fields to satisfy Faraday’s Law
  Automatically includes magnetic field inductance
Conductivity Features of Ocean (grey)
Induced Magnetic Gradient Features
(rainbow)
Magnetic field Vectors

## Slide 14: Approach to Modeling
Spatial distributions of Magnetic fields, conductivity, electrical currents are decomposed into spherical harmonics
  Avoids issues with boundary conditions, gridding volume
  Only need to model surface of sphere
Fourier analysis is uses to compose Time dependence into different frequencies, represented as phasors
  Spatial harmonics are encoded as phasors to represent time dependence
Modeled only toroidal currents on surface
  Normal fields produce toroidal currents
Assuming poloidal currents are negligible
  Poloidal = diverging currents, no curl
  Poloidal current implies charging and capacitance on the surface
  Perhaps variations in conductivity can cause some divergence, which is neglected
  Plan to validate this assumption
Spherical Harmonics

## Slide 15: Calculations in Harmonic Space and Visualizations on Sphere
Start with a distribution of conductivity in “ocean”
  Represent as a sum of spherical harmonics
  Example: (1) Uniform + 5% in higher harmonic
  (Y10,2+ Y10,-2 )
Apply oscillating magnetic field
  Model: Z axis, 10 hours, 1uT
  Mag field normal to sphere is used in computations (2)
Compute Electric field on Surface (3)
Find self consistent solution
  Induced current harmonics (4)
  Emitted mag. field by currents (5)
Calculate gradient of emitted fields (6)
Gradient provide
  Information about conductivity of oceans
  Modeling of expected signals measurable by gradiometer
(1)
(2)
(3)
(4)
(5)
(6)

## Slide 16: Multiple Conductivity Spatial Harmonics
Any conductivity distribution is modeled as a sum of harmonics
The harmonics combine nonlinearly with the ambient magnetic field harmonics to produce the emitted magnetic field
Features in the conductivity show up in the gradient data
Note that the plots of the gradients only show mean amplitudes
Really, the gradients contain much richer information than plotted:
  3x3 tensors
  Amplitude and phase information
  Frequency dependent
The full gradient tensor can be measured to gleam information about the magnetic sources
(1)
(2)
(3)
(4)
(5)
(6)

## Slide 17: Magnetometer Requirements
5% variations in conductivity could produce gradients ~ few pT
  Want to resolve gradients of ~ 1 pT/m to measure 5% variations
Bandwidth:
  0 to 9 mHz used to resolve 160 km surface regions shown every 140 seconds
1 m size gradiometer requirements:
  Fits on a single space craft
  1/f noise requirement: 300 fT / root Hz at 1 Hz
  Well within capabilities of HTS SQUID magnetometers (22 fT/ root Hz @ 1 Hz)
1 km size gradiometer
  Two or more spacecraft
  1/f noise requirement 400 pT/ root Hz
  Well within the capabilities of fluxgate magnetometers (100 pT / root Hz @ 1 Hz)
Gradiometer sensitivity scales linearly with size, so long as it is smaller than the feature size you would like to detect
Features much smaller than the altitude of the space craft will be hard to detect due to 1/r^4 scaling of magnetic gradients
5% variations in conductivity (RMS)
Induced Magnetic Gradient Features several pT/m
(rainbow)

## Slide 18: SQUID Technology
Superconducting Quantum Interference Device
Electric current quantum tunnels through the two insulating junctions
Tunneling depends on quantum interference of (+) and (-) waves
How the waves interfere depends on the magnetic flux in the loop area
  Flux shifts the phase of (-) wave compared to (+) wave
  Modulates the tunnel current
Extremely well calibrated: because depends on area of loop and flux quantum (h/2e)
sensitive and very fast
Our proposed implementation: High Temperature Superconductor (HTS) SQUID system
  Demonstrated 77K sensitivity: 1000 X more sensitive than ECM Fluxgates
  30 fT / Hz1/2 noise
  Much larger frequency range compared other technologies (0 – 10s of MHz) such as search coils
(+)
(-)
Magnetic Flux into loop
Phase shifts depend on magnetic flux
Wave of superconducting electrons
Wave (+)
Wave (-)
Josephson Junctions: thin layers of insulator which block current
Current

## Slide 19: Implementation on a spacecraft
Couple SQUIDs with appropriate input coils are smaller than ~1mm
Wrap on in a 4 cm scale XYZ package to measure magnetic field vector in three dimensions
Mount multiple of these XYZ on a spacecraft boom
Electronic readout
Low noise HTS SQUID
(<1 mm)
Package of 3 for X, Y, Z components, with input coils , shielding etc. (~4 cm x 4cm x 4 cm)

## Slide 20: Fluxgate Technology
ECM sensors
Fluxgate magnetometers such as The Europa Clipper Magnetometer work by applying an alternating magnetic field to a magnetic material
The ambient magnetic field adds to the applied field to determine how the magnetization saturates during each cycle.
The magnetization is measured by a readout circuit to find the ambient field
Placing these magnetometers on different spacecraft with km of separation would provide a sensitive measurement of the magnetic gradient (pT/m level)
About 1000 X less sensitive than SQUIDs, but workable with a long baseline
Polarized
Reversed polarization
8 kHz
Cycle
(magnetic
domains)
Onset of saturation is a measure of the ambient field

## Slide 21: Gradiometer Implementations
Option 1: Single Spacecraft
  Gradiometer is ~20-meter boom
  Requires a sensor with sub pT level noise
  Relatively Insensitive to solar wind noise
  We present this option
Option two: Twin Spacecraft km apart
  Gradiometer distance is between the spacecraft
  Allows for a less sensitive magnetometer
  Requires coordination between spacecraft
  More susceptible to solar wind noise
  Not yet investigated
10 m
2 km
A magnetic gradiometer
Measures the change in magnetic field across a length of the gradiometer
Filters out the large-scale features to detect the local small-scale features.
With signal processing, can also filter out spacecraft generated noise.

## Slide 22: Conclusions
Magnetic Gradiometry may open a new window into oceans worlds hidden under the ice.
We described an implementation using high HTS SQUIDs.
Requires gradiometer and spacecraft design to reduce unwanted noise.
Numerical modeling confirms detection of realistic signals from ocean features is feasible.
Targets for the gradiometer technology include
  Subsurface ocean mapping, subsurface lakes, ocean convection, hydrothermal vents, saline gradients,
  weakly magnetic asteroids
In addition, SQUID technology has other applications which require increased sensor performance:
  Broadband planetary plasma magnetics measurements
  Heliopause measurements

## Slide 23: Back Up Slides

## Slide 24: Orbital Properties
Sample the magnetic field from orbit
  100 km altitude
  Orbital period = 2.086 hours
  speed = 1389.215 m/s
Initial Modeling used 160 km ground pixels (not shown)
node drift per orbit = 1.605 nodes
  114 s crossing time
Orbit 100 km above surface

## Slide 25: Europa’s Response to Jupiter Field as Seen by Galileo
Measure magnetic response
Khurana et al.: Electromagnetic Induction from Europa’s Interior
The Galileo Spacecraft observed a magnetic response from Europa
Margaret Kivelson Group at UCLA identified a dipole signal from Europa
Attributed to salty oceans under several km ice
Conductive ocean response to oscillating field from Jupiter
Potentially habitable world
We would like to know more about the subsurface ocean
Inferred conductive ocean under the ice of Europa

## Slide 26: Conductors Respond to Magnetic Fields
Application of a changing magnetic field on a conductor induces an electrical current in that conductor
The electrical current induces a magnet field that opposes the changed in the magnetic field
The amount of field induces depends on
  The area of the conductor
  Its electrical conductivity
  The rate at which the magnetic field is changing
Measurements of the response can be used to infer the presence of an electrically conductive material, as in a metal detector.
Even works if the conductor is a planetary sized object like a salty ocean
Applied Field Changes
Electric current
Magnetic Response

## Slide 27: About the ECM Fluxgates
  Key Parts
    Rings of soft magnetic alloy which magnetize in an external field
    Drive and sense coils that detect the magnetization
    Employed lots of plastics and adhesives with carbon added for moderate conductivity to provide shielding and protect against IESD
    Use of metal was minimized
  Temperature: regulated to -110 C at Jupiter
Two magnetic rings, with sense 3 coils to detect magnetization in X, Y, Z directions

## Slide 28: Heliopause measurement
Magnetic Measurements out at the heliopause require more sensitivity because magnetic fields are very small
However, would take decades to get there

## Slide 29: Europa Clipper Magnetometer Measurements
Ocean Model
The planned measurements will provide information about the
  Ocean depth
  Salinity
Magnetic response is measured from flybys of the Europa Clipper
Fit a model of the ocean’s magnetic response to the magnetic field data to find these parameters
What is possible with more sensitive magnetometry?

## Slide 30: Issue 2: Spacecraft noise
Issue: Spacecraft noise can dominate over magnetic field
Solution: 1 fitting data from several sensors can separate out this noise from the ambient field
  Numerical simulation shows that fitting magnetic field of several sensors can effectively separate spacecraft fields from ambient field
  Fit to simple multipole expansion to find B
    f= B+c/r3 + d/r4 + e/r5
  Removes random sources of noise near center of spacecraft to find unknown external field B to sub pT levels
Spacecraft Design
  Short Coax cables should have very low emissions
  Block low frequencies with capacitors and use ac electronics
  Concentrate digital circuity in small shielded boxes
  Power with stable ac or DC circuits whose frequency content is not greatly affected by varying loads
  Ideally signaling is via fiber optic
  Chopping: Also, could rotate spacecraft to separate signal from noise
EC Spacecraft Magnetic noise (C. Cochrane)
Fit curve to simulated field measurements in from numerical model .
Random noise sources near S/C center

## Slide 31: Issue 3: Low Temperature Operation
SQUIDs Gradiometer must operate at 80 K or below
Solutions:
  Passive cooling possible
  NEO surveyor will passively cool IR detector arrays to 40 K at Earth Lagrange point (L1)
  Cooling tiny SQUIDs, which use nW of power, is much easier
  Objects at Saturn and Uranus are typically below 80 K
Closer to the sun, cryocoolers are also an option
  Small cryo coolers are available that weight 1.2 kg and use 30 W
NEO Surveyor

## Slide 32: Issue 4. Tolerance to Noisy Environments
Issue: Can Quantum interference devices handle a noisy magnetic environment?
A variant of YBCO Squids called Josephson Junction arrays work in high field environments
  UC Riverside reports “developing superconducting magnetometers designed … with enough dynamic range to operate unshielded with background magnetic fields, such as that of the Earth”
  Replace SQUID loop with a tiny junction only device
  Effective size of junctions is small enough that that flux doesn’t saturate (microns)
Earth field

## Slide 33: Solar Wind model
My simulations of gradiometer performance incorporate a solar wind model
Taylor frozen flow model:
  Solar wind drags magnetic field lines with it.
  Field is not changing in a comoving frame
Power spectrum of solar wind magnetic field noise is well known
  . (Source: Daniele Telloni, “Frequency Transition From Weak to Strong Turbulence in the Solar Wind”) (Near Earth)
Given the power spectrum and velocity of the solar wind , the simulations calculate the spatial variations in the magnetic field
Shows that gradiometer effectively filters our solar wind magnetics
Solar Wind Power Spectrum

## Slide 34: Asteroids– Ceres model

## Slide 35: Detecting Subs
Assume a steel sub 500 m , with magnetism reduce by 100X through heroic effort
Assume 10 m/s boat or aircraft near surface of ocean
Magnetic Field from sub is at surface only 5 ppm of Earths Dipole field at surface
Sample every 300 m / 30 seconds for 30 mHz sampling bandwidth
First order gradiometer:
  Gradient from sub is ~12% of Earth Dipole field
  Sub is detectable from surface of Earth or low flying drone
  1 m first order gradiometer
  Magnetometer 1/f noise requirement ~ 7 pT/Hz1/2 @ 1 Hz
  Well within capabilities of HTS SQUID magnetometers (22 fT/ root Hz @ 1 Hz)
  Not sure if devices that can tolerate Earths field have this sensitivity.
Second order gradiometer to help separate from earth field
  Gradient from is 2600 X Earth field gradient
  2 m second order gradiometer
  Magnetometer noise requirement: 1/f noise ~ pT/Hz1/2 @ 1 Hz
  Well within capabilities of HTS SQUID magnetometers
  Not sure if devices that can tolerate Earths field have this sensitivity.
  Need to get 1/f noise of UCR devices that can handle ambient fields

## Slide 36: Meteor Search
1 meter long Second order gradiometer should be able to detect 1 kg meteor at 20 m below thee surface
  Meteor second derivative should be 10000 X Earth dipole field
  Magnetometer 1/f requirement 60 fT/ Hz
  Well within capabilities of HTS SQUID magnetometers
  Not sure if devices that can tolerate Earths field have this sensitivity.

## Slide 37: Buried Meteors

## Slide 38: Junk?

## Slide 39: Follow Up Mission: Europa Clipper
1
Europa Clipper Magnetometer (ECM) on boom
ECM sensors
Three fluxgate magnetometers located on a boom to isolate from spacecraft magnetics
The planned measurements will provide information about the
  Ocean depth
  Salinity
What could we do with much more sensitive magnetometers?
Notes: Possible hand over to Karen
Harness builds 3 sets. One set delivered to ECM. One set split to vault (int/ext), prop mod, and boom.
ECM test and cal on spare.
E2E electrical on actual flight cable.

## Slide 40: Science Beyond Fluxgate Technology
What could be detected with a much more sensitive technology?

## Slide 41: Numerical Model of Solar Wind Magnetic Noise
Noise varies greatly on large scales:
Hardly varies at all on the scale of a 10 m long gradiometer
~100 nT
~500 fT
A gradiometer measures differences in field across its length (A-B)
Gradiometer filters out large scale variations, but detects small scale ones
Should be able to detect gradients of size 100 fT/ meter or larger
Back of the envelope calculations: conductive features of Europa to generate gradients detectible at 50 km altitude
A
B

## Slide 42: Fluxgates: Operating Principle and Noise
Fluxgates contain a soft magnetic material
Magnetic domains align with external magnetic field
Hysteresis: Domains do not perfectly align; they lag behind the external field
Small hysteresis at large fields because all domains are aligned, larger at zero field
ECM fluxgate apply associating field at 8 kHz.
Hysterics loop causes a magnetic response at 16 kHz (and other multiples)
The 16 kHz signal depend on the strength and direction of the external field
The signal has some noise because domains flips have some randomness (~30 pT / Hz-1/2)
Strong Magnetic field
Reversed Strong
Magnetic field
No external field
8 kHz
Cycle
Magnetization Curve
Intrinsic noise due to magnetic domain realignment
(magnetic
domains)