## Slide 1: Gradiometers for Planetary Science
Mark Lindeman 2-20-2026

## Slide 2: About Magnetic Gradiometers
A magnetic gradiometer measure the difference of magnetic field over a moderate distance
A first order gradiometer
  measures the first derivative
  Selects for local sources because signals fall off as R-4
This measurement results produces the magnetic field gradient tensor
  Traceless 3x3 symmetric tensor
  In source free region, there are only 5 independent components
Can measure this with 3 vector magnetometers, with (4 redundant measurements)
OK to only use a pair of magnetometers
  Gives one component of the tensor, but that is still useful
  Can rotate the gradiometer to get the full tensor, if needed
Second order gradiometers measure the second derivative,
  Requires more sensors, with higher sensitivity
  More strongly selects for local source because signal falls as R-5
B1
B2
B3
B1
B2

## Slide 3: Jupiter Is a Huge Rotating Magnet
Jupiter's magnetic field is hundreds of nanotesla (nT) at Europa's orbit
Induces electrical currents in conducting materials
The Galileo Spacecraft observed a magnetic response from Europa
Margaret Kivelson Group at UCLA identified a magnetic dipole signal from Europa
Attributed to salty oceans under several km ice
Europa's
Magnetic Response
Ocean Model
Jupiter Magnetic Field

## Slide 4: Idea: Features May Induce Significant Magnetic Gradients
Jupiter applies a varying magnetic field to Europa
This induces electrical current in conductive regions (of ocean)
Spatial variation in conductivity results in local variations in the magnetic field gradient
These local features can have a steeper gradient than nonlocal large-scale fields from distant sources
Provides a sensitive probe of local variations in conductivity or magnetism under the surface
A first order gradiometer measures the first derivative of the magnetic field, which is large near sources but falls off as R4
External field from Jupiter or Solar Wind
(blue)
Induced field gradient from conductive regions
(green)
The induced magnetic field has a larger gradient than the solar wind field
Conductive Region

## Slide 5: Some Applications

## Slide 6: Water World Magnetic Gradients from Orbit
Conductivity Features of Ocean (grey)
Induced Magnetic Gradient Features
(rainbow)
Magnetic field Vectors
Orbit 100 km above surface
Measure Magnetic Gradients to Observe Magnetic Features
Gradient contains detailed information about planetary magnetism, induced currents, and conductivity

## Slide 7: Propose to Search for Magnetic Features of Water Worlds
Magnetic environment induces currents in conducting features
Look for magnetic signals due to
  Water in lakes and veins in the ice
  Variations in ocean depth
  Geysers
  Ocean floor vents
  Magnetic signals due to water flowing (magnetohydrodynamics)
  Subsurface electrical currents

## Slide 8: Convection and Geology
Predicted underwater plumes of highly saline water
Predicted convection, layering, diffusion dynamics in Europan ocean
  Primarily composed of aqueous Na2SO4 and MgSO4, both saturated and dilute concentrations
Expect greatly varying conductivity in plumes, layers, and currents
Should result in fine-scale magnetic signals

## Slide 9: Uranus System
The Uranus system is highlighted in the Decadal Survey
Moons are likely water worlds, and targets for detailed magnetic surveying:
  Ariel
  Umbriel
  Titania
  Oberon
Also, the Magnetosphere of Uranus offers interesting plasma physics to study between visits to moons
Uranus and Moons

## Slide 10: New Asteroid Science:
Ceres is a possible water world
  Geological features suggest brine under the ice
  Solar wind may induce a weak magnetic response from the subsurface brine
Previously undetectable asteroids
  Fluxgates did not detect magnetism from weakly magnetic asteroids
  These include on Eros, Lutetia, 67P, Braille, Steins, etc.
  Map the weak magnetic fields of these objects
  Provide evidence about composition and evolution
Solar wind induces signals from metallic parts
Eros

## Slide 11: Detecting Terrestrial Magnetic Objects By Gradients
Nuclear subs:
  Low magnetism Sub, 300 meters deep oceans can be detected
    (Assume 1 % of magnetization of iron)
  1st order Gradient from the sub is ~12% of Earth's dipole field gradient
  2nd order gradiometer: the sub is 2600X earth dipole field gradient
  Detectible by ~1 m SQUID gradiometers
  Place on boat, buoy, or drone
Meteors and geological features
  1 kg iron meter 20 m underground could be detected with similar technology

## Slide 12: Why Use Magnetic Gradiometer for Water Worlds?
Picks out nearby sources like magnetic areas in planetary objects
Detects electrically conductive regions through their magnetic response to ambient fields
Even though the magnetic field is very smooth, the gradient is not smooth
  Provides information about the magnetic structure of the body
Filters out large scale noise sources like the solar wind
5% variations in ocean conductivity produce pT/m gradients
Conductivity of Ocean (grey)
Induced Magnetic Gradient at 100 km (rainbow)
Magnetic field Vectors

## Slide 13: Magnetic Noise in Space
External-field variability may overwhelm magnetic signals, but not overwhelm the gradients
  Solar wind is a source of magnetic noise varying up to 100 nT level near Earth
  nT magnetic fluctuations dominate over the signals we want to detect from ocean worlds
  Though the magnetic field varies a lot over time, it is fairly uniform on meter to kilometer spatial scales
  In our initial modeling, we assume the solar wind as representative of external magnetic fields
We use a gradiometer configuration to effectively null out these long-range fields
  Local magnet sources have a significant gradient on this scale
  Large scale, far away magnetic sources have small gradients, decreasing as R-4

## Slide 14: Filtering by Gradiometer
Gradiometer removes long wavelength, low frequency magnetic signals such as from solar wind
Removes long term correlations in the noise
Preserves signals from nearby magnetic sources
  These have much steeper gradients
Modeling predicts solar wind noise is filtered to ~1 fT/m
  Easily sufficient to measure planetary magnetic gradients
Suppress
Raw Solar Wind Noise
Filtered Solar Wind Noise

## Slide 15: Modeling of Gradients

## Slide 16: Magnetic Field Model
We modeled magnetic field gradients of a Europa-like body to verify implementation is practical
Conductivity is modeled as a thin shell
Modeled ambient oscillating magnetic field similar to Jupiter field on Europa
Faraday's law: changing magnetic fields normal to the surface induce toroidal electric currents on the sphere
  Toroidal = no divergence, has curl
Electric current produces emitted fields
Solve self-consistently for currents and emitted fields to satisfy Faraday's law
  Automatically includes magnetic field inductance
Solver is custom built in python
Validated against analytical solutions and symmetry tests
Conductivity Features of Ocean (grey)
Induced Magnetic Gradient Features
(rainbow)
Magnetic field Vectors

## Slide 17: Approach to Modeling
Spatial distributions of Magnetic fields, conductivity, electrical currents are decomposed into spherical harmonics
  Avoids issues with boundary conditions, 3D gridding
  Only need to model harmonics on 2-D surface of sphere
Fourier analysis is used to decompose time dependence into frequencies
  Coefficients of the spatial harmonics are encoded as phasors to represent time dependence
Modeled only toroidal currents on surface
  Radial magnetic component produce toroidal currents
Assuming poloidal currents are negligible
  Poloidal = diverging currents, no curl
  Poloidal current implies charging and capacitance on the surface
  Perhaps variations in conductivity can cause some divergence, which is currently neglected
  Plan to validate this assumption
Spherical Harmonics

## Slide 18: Calculations in Harmonic Components and Visualizations
Start with a distribution of conductivity in 'ocean’
  Collapse to a surface conductivity
  Represent as a sum of spherical harmonics (Yl,m )
  Example: (fig. 1) Uniform (Y0,0) + 5% in higher harmonics (Y10,2+ Y10,-2 )
Apply oscillating magnetic field
  Z axis oscillating magnetic field component (Y1,0 ) (fig. 2)
  10-hour period, 1 uT amplitude
Compute resulting electric field on Surface (fig. 3)
Find self-consistent solution
  Induced current harmonics (fig.4)
  Emitted mag. field by currents (fig. 5)
Calculate gradient of emitted fields (fig. 6)
Gradients provide Information about conductivity of oceans
(1)
(2)
(3)
(4)
(5)
(6)

## Slide 19: Multiple Conductivity Spatial Harmonics
Any conductivity distribution is modeled as a sum of harmonics
The harmonics combine nonlinearly with the ambient magnetic field harmonics to produce the emitted magnetic field
Features in the conductivity show up in the gradient data
Note that these plots of the gradients only show mean amplitudes
Really, the gradients contain much richer information than plotted:
  3x3 tensors
  Amplitude and phase information
  Frequency dependent
Either the full gradient tensor or partial information can be measured to glean information about magnetic sources.
(1)
(2)
(3)
(4)
(5)
(6)

## Slide 20: Gradiometer Implementation

## Slide 21: Gradiometer Requirements
Option 1: Single Spacecraft, 1 m long Gradiometer
Noise requirements:
  White noise < 7.7 pT / √Hz @ 1 Hz
  1/f noise < 380 fT / √Hz @ 1 Hz
Use HTS SQUID magnetometers
  White noise: ~ 20 fT / √Hz
  1/f noise ~22 fT / √Hz @ 1 Hz
Option 2: Paired spacecraft, 1 km apart
Noise requirements:
  White noise < 7.7 nT / √Hz
  1/f noise requirement: < 7.7 pT / √Hz @ 1 Hz
Use fluxgate magnetometers
  White noise: ~50 pT / √Hz
  1/f noise: 100 pT / √Hz @ 1 Hz
1 m
1 km
Want to resolve gradients of ~ 1 pT/m to measure 5% variations in ocean conductivity
Bandwidth: 0 to 9 mHz used to resolve 160 km surface regions shown every 140 seconds
Well within the capabilities of existing magnetometers
Option 3: 10 m boom, rotating flux gates to modulate signal @ 10 Hz, above 1/f noise
Noise requirements:
  White noise < 77 nT / √Hz n/f noise
Use fluxgate magnetometers
  White noise: ~50 pT / √Hz
10 m
SQUIDs
Fluxgates
Rotating
Fluxgates

## Slide 22: SQUID Technology
Superconducting Quantum Interference Device
Electric current quantum-tunnels through two insulating junctions
Tunneling depends on quantum interference of (+) and (-) waves
How the waves interfere depends on the magnetic flux in the loop area
  Flux shifts the phase of (-) wave compared to (+) wave
  Modulates the tunnel current
Extremely well calibrated: because depends on area of loop and flux quantum (h/2e)
Sensitive and very fast
Our proposed implementation: High Temperature Superconductor (HTS) SQUID system
  Demonstrated 77K sensitivity: 1000 X more sensitive than ECM Fluxgates
  30 fT / Hz1/2 noise
  Much larger frequency range than other technologies (0 to tens of MHz), such as search coils
(+)
(-)
Magnetic Flux into loop
Phase shifts depend on magnetic flux
Wave of superconducting electrons
Wave (+)
Wave (-)
Josephson Junctions: thin layers of insulator which block current
Current

## Slide 23: Implementation on a spacecraft
Couple SQUIDs with appropriate input coils are smaller than ~1mm
Wrap one in a 4 cm-scale XYZ package to measure the magnetic field vector in three dimensions
Mount multiple XYZ packages on a spacecraft boom
Electronic readout
Low noise HTS SQUID
(<1 mm)
Package of 3 for X, Y, Z components, with input coils , shielding etc. (~4 cm x 4cm x 4 cm)

## Slide 24: Fluxgate Technology
ECM sensors
Fluxgate magnetometers such as The Europa Clipper Magnetometer work by applying an alternating magnetic field to a magnetic material
The ambient magnetic field adds to the applied field to determine how the magnetization saturates during each cycle.
The magnetization is measured by a readout circuit to find the ambient field
Placing these magnetometers on different spacecraft with km of separation would provide a sensitive measurement of the magnetic gradient (pT/m level)
About 1000 X less sensitive than SQUIDs, but workable with a long baseline
Polarized
Reversed polarization
8 kHz
Cycle
(magnetic
domains)
Onset of saturation is a measure of the ambient field

## Slide 25: Spacecraft noise
Issue: Spacecraft noise can dominate the magnetic field
Spacecraft Design
  Short Coax cables should have very low emissions
  Block low frequencies with capacitors and use ac electronics
  Concentrate digital circuitry in small shielded boxes
  Power with stable ac or DC circuits whose frequency content is not greatly affected by varying loads
  Ideally signaling is via fiber optic
  Chopping: Could rotate spacecraft to separate signal from noise
Fitting data from several sensors can separate this noise from the ambient field
  Numerical simulation shows that fitting magnetic field of several sensors can effectively separate spacecraft fields from ambient field
Gradiometer using paired spacecraft greatly reduces impact of spacecraft noise
EC Spacecraft Magnetic noise (C. Cochrane)

## Slide 26: Conclusions
Magnetic gradiometry may open a new window into ocean worlds hidden under ice
Subsurface ocean mapping of subsurface lakes, ocean convection, hydrothermal vents, saline gradients
Targets for gradiometer technology
  Weakly magnetic asteroids
  Terrestrial magnetic objects such as subs, meteors, and geological formations
Observable at the pT/m sensitivity
Calculations indicate that existing magnetometers can enable magnetic radiometry
  SQUIDs or Fluxgates could be used depending on the implementation

## Slide 27: Back Up Slides

## Slide 28: Orbital Properties
Sampling the magnetic field from orbit
  100 km altitude
  Orbital period = 2.086 hours
  speed = 1389.215 m/s
Initial Modeling used 160 km ground pixels (not shown)
node drift per orbit = 1.605 nodes
  114 s crossing time
Orbit 100 km above surface

## Slide 29: Detecting Terrestrial Magnetic Objects
Assume a 500 m steel submarine, with magnetism reduced by 100x through major mitigation
Assume 10 m/s boat or aircraft near surface of ocean
Magnetic field from the sub at the surface is only 5 ppm of Earth's dipole field
Sample every 300 m / 30 seconds for 30 mHz sampling bandwidth
First order gradiometer:
  Gradient from the sub is ~12% of Earth's dipole field gradient
  The sub is detectable from Earth's surface or a low-flying drone
  1 m first order gradiometer
  Magnetometer 1/f noise requirement ~ 7 pT/Hz1/2 @ 1 Hz
  Well within capabilities of HTS SQUID magnetometers (22 fT/ sqrt(Hz) @ 1 Hz)
  Research to learn if devices that tolerate Earth's field have this sensitivity. May have to use bucking coils
  Need measured 1/f noise for UCR devices that can handle ambient fields
Second-order gradiometer to help separate from Earth's field
  Gradient is 2600x Earth's field gradient
  2 m second order gradiometer
  Magnetometer noise requirement: 1/f noise ~1 pT/Hz^1/2 @ 1 Hz
  Well within capabilities of HTS SQUID magnetometers

## Slide 30: Europa's Response to Jupiter Field as Seen by Galileo
Measure magnetic response
Khurana et al.: Electromagnetic Induction from Europa's Interior
The Galileo Spacecraft observed a magnetic response from Europa
Margaret Kivelson Group at UCLA identified a dipole signal from Europa
Attributed to salty oceans under several km ice
Conductive ocean response to oscillating field from Jupiter
Potentially habitable world
We would like to know more about the subsurface ocean
Inferred conductive ocean under the ice of Europa

## Slide 31: Conductors Respond to Magnetic Fields
Application of a changing magnetic field on a conductor induces an electrical current in that conductor
The electrical current induces a magnetic field that opposes the change in the magnetic field
The amount of induced field depends on
  The area of the conductor
  Its electrical conductivity
  The rate at which the magnetic field is changing
Measurements of the response can be used to infer the presence of an electrically conductive material, as in a metal detector.
Even works if the conductor is a planetary sized object like a salty ocean
Applied Field Changes
Electric current
Magnetic Response

## Slide 32: About the ECM Fluxgates
  Key Parts
    Rings of soft magnetic alloy which magnetize in an external field
    Drive and sense coils that detect the magnetization
    Employed lots of plastics and adhesives with carbon added for moderate conductivity to provide shielding and protect against IESD
    Use of metal was minimized
  Temperature: regulated to -110 C at Jupiter
Two magnetic rings, with sense 3 coils to detect magnetization in X, Y, Z directions

## Slide 33: Fluxgates: Operating Principle and Noise
Fluxgates contain a soft magnetic material
Magnetic domains align with external magnetic field
Hysteresis: Domains do not perfectly align; they lag behind the external field
Small hysteresis at large fields because all domains are aligned, larger at zero field
ECM fluxgates apply an oscillating field at 8 kHz.
The hysteresis loop causes a magnetic response at 16 kHz (and other multiples)
The 16 kHz signal depends on the strength and direction of the external field
The signal has noise because domain flips are partly random (~30 pT/Hz^1/2)
Strong Magnetic field
Reversed Strong
Magnetic field
No external field
8 kHz
Cycle
Magnetization Curve
Intrinsic noise due to magnetic domain realignment
(magnetic
domains)

## Slide 34: Heliopause measurement
Magnetic Measurements out at the heliopause require more sensitivity because magnetic fields are very small
However, would take decades to get there

## Slide 35: Europa Clipper
1
Europa Clipper Magnetometer (ECM) on boom
ECM sensors
Three fluxgate magnetometers located on a boom to isolate from spacecraft magnetics
The planned measurements will provide information about the
  Ocean depth
  Salinity
What could we do with much more sensitive magnetometers
Notes: Possible hand over to Karen
Harness builds 3 sets. One set delivered to ECM. One set split to vault (int/ext), prop mod, and boom.
ECM test and cal on spare.
E2E electrical on actual flight cable.

## Slide 36: Issue 3: Low Temperature Operation
A SQUID gradiometer must operate at 80 K or below
Solutions:
  Passive cooling possible
  NEO surveyor will passively cool IR detector arrays to 40 K at Earth Lagrange point (L1)
  Cooling tiny SQUIDs, which use nW of power, is much easier
  Objects at Saturn and Uranus are typically below 80 K
Closer to the sun, cryocoolers are also an option
  Small cryocoolers are available that weigh 1.2 kg and use 30 W
NEO Surveyor

## Slide 37: Issue 4: Tolerance to Noisy Environments
Issue: Can quantum interference devices handle a noisy magnetic environment
A variant of YBCO SQUIDs, called Josephson junction arrays, works in high-field environments
  UC Riverside reports "developing superconducting magnetometers designed … with enough dynamic range to operate unshielded with background magnetic fields, such as that of the Earth"
  Replace the SQUID loop with a tiny junction-only device
  The effective junction size is small enough that flux does not saturate (micron scale)
Earth field

## Slide 38: Solar Wind Model
My simulations of gradiometer performance incorporate a solar wind model
Taylor frozen flow model:
  Solar wind drags magnetic field lines with it.
  Field is not changing in a comoving frame
Power spectrum of solar wind magnetic field noise is well known
  . (Source: Daniele Telloni, "Frequency Transition From Weak to Strong Turbulence in the Solar Wind") (Near Earth)
Given the power spectrum and velocity of the solar wind , the simulations calculate the spatial variations in the magnetic field
Shows that a gradiometer effectively filters out solar-wind magnetic noise
Solar Wind Power Spectrum

## Slide 39: Numerical Model of Solar Wind Magnetic Noise
Noise varies greatly on large scales:
Hardly varies at all on the scale of a 10 m long gradiometer
~100 nT
~500 fT
A gradiometer measures differences in field across its length (A-B)
Gradiometer filters out large scale variations, but detects small scale ones
Should be able to detect gradients of size 100 fT/ meter or larger
Back of the envelope calculations: conductive features of Europa to generate gradients detectible at 50 km altitude
A
B

## Slide 40: Asteroids - Ceres Model

## Slide 41: Additional Ideas
Are their significant electrical currents in aquifers?
Do poiloidal currents charge Europa enough to have a significant E field?